## Slide 1: C1: Introduction to ARM

## Slide 2: Outline
Intro to ARM architecture
Arithmetic and Bitwise Instructions
Shift Instructions
Loads/Stores and addressing modes
Conditions and Predicated Instructions
Function calls and returns
Program examples
Notes: This set of slides does not show the full details of the instruction set. Other materials within this module give more detail. Also the ARM website has very detail instruction set descriptions. (URL)

## Slide 3: ARM holdings
Originally stood for Acorn RISC machine, then Advanced RISC Machines
ARM holdings is a British semi-conductor and software design company.
They design. Others license and manufacture
Microcontrollers, CPUs, GPUs
Leader in intellectual property core licensing
Now owned by Japan’s Softbank group
The “ARM architecture” includes a variety of different designs and models.
Notes: https://www.eenewsanalog.com/news/arm-loses-ip-market-share-fast-growing-followers

## Slide 4: Raspberry PI-3
Broadcom BCM2837 – ARM licensee and manufacturer of CPU
Uses ARM Cortex A-53
  ARM v8-A architecture
  32bit or 64bit
1.2 GHz clock speed
Note the SIMD and FPU sub-units
Notes: This slide is current as of 1/2019. Different Raspberry Pi models utilize different Broadcom parts. Different Broadcom parts utilize different versions of the ARM ISA.

## Slide 5: 32-bit ARM architectural features
16 32-bit general purpose registers. R0-R15
Three of these have special purposes:
  R13 – default Stack Pointer (SP)
  R14 – Link Register (LR)
  R15 – Program Counter (PC). Avoid modifying
Three-stage pipeline model (though actual pipeline much deeper)
Load/Store model
Can be configured as big or little endian
Predicated Instructions
Optional floating point co-processor (VFP)
Optional integer SIMD unit (NEON)

## Slide 6: Arithmetic Operations
General format:
  <Instruction> <Dest>, <Operand1>, <Operand2>
  <Dest> - always a register R0-R15
  <Operand 1> - R0-R15
  <Operand 2> options
    R0 – R15
    Immediate, e.g., #17
    A shifted value
Examples
  ADD R0, R1, R2 @ R1 + R2 -> R0
  SUB R4, R5, #8 @ R5 – 8 -> R4
@ begins an ARM ASM line comment
Notes: Note: ARM ASM examples shown follow the syntax used by the GNU toolchain. Other assemblers and assembly emulators may have varied syntax for some forms, including the comment character.
The details of the instruction set encoding are not shown in this presentation and are considered beyond the scope of this module. They an be

## Slide 7: Arithmetic Operations
ADD <dest>, <Operand1>, <Operand2> - Addition
ADC <dest>, <Operand1>, <Operand2> - Addition + Carry bit
SUB <dest>, <Operand1>, <Operand2> - Subtraction
  <Operand1> - <Operand2>
RSB <dest>, <Operand1>, <Operand2> - Reverse Subtraction
  <Operand2> - <Operand1>
MUL <dest>, <Operand1>, <Operand2> - Multiplication
  <dest> cannot be the same as <Operand1>
  <Operand2> must be a register.
MLA <dest>, <Operand1>, <Operand2>, <sum> - Multiply and Accumulate
  <dest> = <sum> + <Operand1> * <Operand2>
  Same restrictions as MUL
Notes: This is just a laundry list of the most common arithmetic instructions. It is possible to skip this slide and point the students to other documentation.

## Slide 8: Bit-wise Instructions
AND <dest>, <Operand1>, <Operand2> - Bitwise Logical And
ORR <dest>, <Operand1>, <Operand2> - Bitwise Logical Or
EOR <dest>, <Operand1>, <Operand2> - Bitwise Exclusive Or (XOR)
BIC <dest>, <Operand1>, <Operand2> - Bit clear
MVN <dest>, <Operand1> - Move negative, performs logical NOT
Notes: And, or, and xor (eor) work like you would expect. Bit-clear is different. The bit-clear instruction is dependent on the order of its operands. In short, if we consider Operand1 and Operand2 as a sequence of bits, let O1n be the bit in position n of operand1 and O2n be the bit in position n of Operand 2. Let Dn be bit n in the destination. If O2n == 0 then Dn = O1n else (O2n == 1) Dn = 0. That is, if the bit n in Operand 2 is a 0, then copy the corresponding bit in Operand1 to the Destination. Otherwise, bit n in operand 2 is 1, put a 0 in the destination. Logically this instruction does this:
<dest> = <Operand1> AND (NOT <Operand1>)
MVN stands for Move negative and effectively performs a bitwise NOT of operand1 and puts the result in <dest>

## Slide 9: Shift Instructions
Shift instructions can be used by themselves or attached to other instructions as an Operand2 modifier. For example:
  ADD R0, R1, R2, LSL #3
  This shifts R2 to the left by three before adding it to R1
LSL – Logical shift left
ASL – Arithmetic shift left (same as LSL)
LSR – Logical shift right
ASR – Arithmetic shift right, copies sign bit to right-most bits
Standalone example
  ASR R0, R1, #2
Notes: Depending on your disassembler these instructions may appear to be encoded differently. A pure shift instruction is really encoded as a MOV with a shifted operand. However, they will typically be shown as a pure shift instruction when disassembled.

## Slide 10: Loads and Stores
Move (copy)
  MOV <dest>, <Operand2>
  MOV R0, R1 @ Copy contents of R1 into R0
Load Register
  LDR <dest>, [<Operand1>]
  LDR R0, [R1] @ Load from memory location pointed to by R1 into R0
Store Register
  STR <src>, [<Operand1>]
  STR R3, [R5] @ Store the contents of R3 into the memory location pointed to by R5
  Note the first operand of STR is the source, which is atypical for ARM instructions.

## Slide 11: Addressing Modes
Indirect addressing
  LDR R0, [R1]
  R1 is a memory address, and we load from that memory location into R0
Pre-indexed addressing
  LDR R0, [R1, #8]
  LDR R0, [R1, R2]
  Add #8 (or R2) to R1 to compute memory location. Load from this new memory location. No change to R1
Pre-indexed addressing with write-back
  LDR R0, [R1, #8]!
  Same as Pre-indexed but updates R1 with new address

## Slide 12: Addressing modes continued
Post-indexed addressing
  LDR R0, [R1], R2
  LDR R3, [R1], #4
  Load from R1. After load is complete add #4 (or R2) to register R1
By default LDR and STR move 4-byte words
To load and store only a single byte, add the B suffix to LDR or STR
  LDRB R0, [R1] @ only load one byte from the memory address pointed to by R1 into R0
  STRB R9, [R4, #5] @ Store one bye into the address pointed at by R4 + 5.

## Slide 13: Current Program Status Register (CPSR)
.. Or just Status Register
Stores info about current program and the results of operations
Four bits are the status flags:
  Bit 31 – N = Negative Flag
    1 result was negative. 0 result was non-negative
  Bit 30 – Z = Zero Flag
    1 result was 0. 0 result was non-zero
  Bit 29 – C = Carry Flag
    Carry-out bit from shifter or ALU
  Bit 28 – V = Overflow Flag
    Signed-arithmetic overflow bit

## Slide 14: Status Flags
Various instructions can change or test these bits
For example:
  BEQ _address @ This will jump to address if the Z flag is 1 (Branch if EQual to zero.)
  BNE _address @ This will jump to address if the Z flag is 0 (Branch if Not Equal to zero.)
CMP <operand1> <operand2>
  Only CMP and CMN directly modify status bits
  Subtracts operand2 from operand1 and throws away the result.
  If result was zero Z flag is set (1) otherwise cleared (0)
  If result was negative N flag is set otherwise cleared.
  Likewise for Overflow and Carry bits
Other instructions can change the status register by adding the ‘S’ suffix to the instruction.

## Slide 15: Predicated Instructions
Most instructions can be predicated by adding a conditional suffix (see table)
For example:
  ADDLT R0, R1, R2 @ Add only if result of compare was < 0
  MOVEQ R0, R2 @ Move only if result of compare was = 0
Suffix | Meaning
EQ | Equal
NE | Not Equal
VS | Overflow Set
VC | Overflow Clear
AL | Always
NV | Never
HI | Higher
LS | Lower than or Same
Suffix | Meaning
PL | Plus Clear
MI | Minus Set
CS/HS | Carry Set
CC/LO | Carry Clear
GE | Greater than or equal to
LT | Less Than
GT | Greater Than
LE | Less than or Equal to

## Slide 16: Predicated Instructions
These condition codes are based on the four status flags.
EQ: Equal Z = 1 (only depends on Z bit)
  Will only run if the Z flag is 1
  Example: CMP R0, R1 MOVEQ R0, #1
LT: Less Than (N=1, V=0 OR N=0, V=1) and Z=0
  This will be true if Operand1 < Operand2 CMP R5, #255 @ compare R5 with 0xFF SUBLT R5,R5,R6 @ if R5 < 0xFF R5 = R5 - R6
Other conditions based on the status bits in similar ways

## Slide 17: Predicated Instructions - Example
If/else constructs can be implemented with branches or with predicated instructions.
Consider this C-style if/else statement and assume the variable ‘a’ resides in R5.
if (a != 0) a = a - 1
else
a = 40
CMP R5, #0
SUBNE R5, R5, #1
MOVEQ R5, #40
CMP R5, #0
BEQ _else
_then SUB R5, R5, #1
BAL _exit
_else MOV R5, #40
_exit …
Implementation using branches
Implementation using predicated instructions

## Slide 18: Functions
Functions must follow the AAPCS standards.
  First four arguments in R0-R3
  Additional arguments passed on the stack
  Return value in R0
  Functions must maintain (or restore) values R4-R12, but can freely modify R0-R3
  Typical to push R4-R12 at start of function and pop at end to preserve them
  Functions must preserve and restore the address in link register to return to caller.

## Slide 19: Writing functions
Functions begin with a label followed by a colon. The end of the function is indicated by a POP {PC} (return) instruction.
  Label:
    PUSH {LR}
    Code
    Code One function
    POP {PC}
  Label2:
Functions begin by pushing the Link Register and end by popping the stack into the Program Counter.

## Slide 20: Writing functions
main: PUSH {LR}
MOV R0, #2 @ Place arguments in appropriate registers
MOV R1, #4
MOV R2, #1
BL Foo @ calling the Foo function
@ …remaining code…
Foo: PUSH {LR} @ preserves LR on stack to return to main function
ADD R0, R1, R2
MUL R0, R1, R0
MOV R2, #3 @ Function is free to modify R2
ADD R0, R0, R2 @ return value in R0.
POP {PC} @ pops stack into PC to return to main function
What is the output of this function?
Notes: The output is 23

## Slide 21: Writing functions
main: PUSH {LR}
MOV R0, #2
MOV R1, #4
MOV R2, #1
BL Foo @ calling the Foo function
@ …remaining code…
Foo: PUSH {LR} @ preserves Link Register on stack to return to main function
ADD R0, R1, R2
MUL R0, R1, R0
MOV R2, #3
ADD R0, R0, R2
POP {PC} @ pops stack into PC to return to main function
BL Foo will set the PC to address of Foo label. At the end of the function, popping to the PC will return the PC to one line after the function call.

## Slide 22: ARM vs. MIPS
ARM | MIPS
16 GP registers | 32 GP registers
Most instructions allow immediate operands | ‘i’ instructions allow immediates otherwise put immediate in a register
Almost every instruction can be executed conditionally | Conditional branches only
Use of explicit CMP (compare) instruction | Instructions (or pseudo-instructions) to do comparison within conditional branch instruction
R3 is a register, #3 is an immediate | $3 is a register, 3 is an immediate
A little more complex | A little simpler/lower power
Little endian (though configurable now) | Big endian
Indirect, pre-indexed, and post-indexed memory addressing modes (load/store) | Base addressing for memory loads and store (essentially ARM’s pre-indexed addressing)
Reduced code size mode (Thumb) | N/A
Notes: These are just a few differences that students may be interested in. Obviously, there are others. Your mileage may vary as various MIPS and ARM versions/implementation will have slightly different feature sets.

## Slide 23: Assembly Code Examples
C/C++
int a = 0;
for(int x = 1; x < 10=; x++)
if (x & 1 == 0)
a = a + x;
MIPS
li $5, 0
li $2, 1
li $3, 10
lp: bgt $2, $3, ex
andi $4, $2, 1
bnez $4, skip
add $5, $5, $2
sk: addi $2, $2, 1
j loop
ex: # other code
ARM
MOV R5, #0 @ use R5 for a
MOV R2, #1 @ use R1 for x
lp: CMP R2, #10
BGT exit
AND R4, R2, #1
CMP R4, #0
ADDEQ R5, R5, R2
ADD R2, R2, #1
BAL loop
ex: @ any other code
Notes: Sum all even positive integers less than or equal to 10.