## Slide 1: C1: Intro to ARM NEON

## Slide 2: Coprocessors
A coprocessor is an auxiliary processing element operating under the direction of the primary CPU.
Certain processor-intensive tasks can be offloaded to the coprocessor to improve overall system performance.
A coprocessor may be used for tasks such as:
  Floating-point operations
  Graphics processing
  Cryptographic processing
  I/O processing
A coprocessor may operate synchronously with the primary CPU or may be independent processors operating asynchronously

## Slide 3: Quick introduction to SIMD
SIMD stands for Single Instruction Multiple Data Stream
The idea is that a single CPU instruction will be executed but multiple instances of that operation will be executed on different pieces of data.
For example, say you wanted to add all the elements in one array to all the elements of another array and store them in a third array.
For(int i = 0; i < 10; i++)
c[i] = a[i] + b[i];
Since each of these additions occur independently from on another we may be able to execute them in parallel

## Slide 4: Quick introduction to SIMD
If we are able to load multiple array values from memory at the same time and have an architecture that supports SIMD operations we could potentially speed up the entire computation.
For example, consider that the arrays a, b, c all contain single bytes, arranged in memory like this
a[0], a[1] …
Assume we have thirty-two bit registers:
  Load 4 values from array into register R0
  Load 4 values from array B into register R1
  Add each of the four elements from R0 to the four elements in R1 and store the result in array c.
  This idea is illustrated in figure ??

## Slide 5: ARM’s NEON coprocessor
The NEON coprocessor implements the Advanced SIMD media processing architecture. Advanced SIMD is an optional part of the ARMv7-A architecture. The components of the NEON coprocessor are:
  NEON register file with 32x64-bit general-purpose registers
  NEON integer execute pipeline (ALU, Shift, MAC)
  NEON dual, single-precision floating-point execute pipeline (FADD, FMUL)
  NEON load/store and permute pipeline

## Slide 6: ARM NEON code development
Developing code for NEON, or any SIMD architecture, typically involves an additional layer of complexity.
As a programmer, there are several ways you can use Neon technology:
  Neon intrinsics (these look like function calls in C/C++ but turn into specific Neon assembly instructions upon compilation)
  Neon-enabled libraries (a set of functions implemented in Neon assembly)
  Auto-vectorization by your compiler (the most “automatic” way to use Neon)
  Hand-coded Neon assembler (leads to good performance but is labor intensive.)

## Slide 7: ARM NEON code examples
Show some NEON instructions and their SISD equivalents

## Slide 8: References
https://developer.arm.com/architectures/instruction-sets/simd-isas/neon
https://developer.arm.com/documentation/ddi0344/k/neon-and-vfp-programmers-model/about-the-neon-and-vfp-programmers-model/neon-media-coprocessor

## Slide 9: Questions
What is SIMD, and how does it improve performance?
What is the “cost” of developing code for NEON?
  Increased code complexity may lead to code that is more difficult to maintain
  Development time is increased.

## Slide 10: Lab
Goals:
  Study how a single chip can offer features that trade-off code-size and performance
  Gain experience using command line tools
  “The ARM ISA inherently possesses heterogeneity in its design”1 and we want to explore that.
In this lab you are given some C code and will build it for ARM, Thumb-1, and Thumb-2.
A makefile is provided for you.
You will:
  Measure the size of the relevant function for the three different ISA’s
  Measure the performance of the code as compiled for the three different ISA’s
  See the 32-bit, 16-bit, and mixed-bit instructions by disassembling the code.
  Summarize your results and answer some questions.
1. Wooseok Lee, Dam Sunwoo, Christopher D. Emmons, Andreas Gerstlauer, and Lizy John Exploring Opportunities for Heterogeneous-ISA Core Architectures in High-Performance Mobile SoCs, University of Texas, Technical report, UT-CERC-17-01 March 10, 2017