## Slide 1: C1: Intro to ARM Thumb

## Slide 2: Thumb introduction
“Thumb mode” was developed as a way to reduce the size of ARM code by trading off speed.
There are various flavors of Thumb
Generally:
  ARM code: all instructions are 32-bit
  Thumb-1 code: all instructions are 16-bit (often simply called “Thumb”)
  Thumb-2 code: mixes 16 and 32-bit instructions
Speed of Thumb-1 vs. ARM code is impacted by the particular memory system of the part.
Thumb-2 is very efficient both in terms of code-size and speed.

## Slide 3: Thumb-1 basics
Subset of the ARM instruction set
All instructions are 16-bits (not 32)
Used when memory is at a premium
Registers are STILL 32 bits
Can move back and forth between ARM code and Thumb code within the same executable
A single bit in the control register is used to select ARM or Thumb mode

## Slide 4: Thumb-1 vs. ARM differences
R0 – R7 freely available, but limited access to other registers
  R8-R12 only with MOV, ADD, SUB, CMP
  Very limited access to R13, R14, R15
  Only indirect access to CPSR
No floating point access
Want to access other registers? Go back to ARM mode
Registers are preserved when switching modes

## Slide 5: Thumb-1 vs. ARM differences
Most instructions in Thumb are two address: ADDS R12, R8, #16 (three address ARM instruction) ADD R2, #3 (two address Thumb1 instruction, dest is implied)
So can’t do this: AND R1, R2, R3
Instead we can write: MOV R1 R3 AND R1 R2
Limited addressing modes
No conditional execution except conditional branch
All instructions implicitly have ‘S’ bit set

## Slide 6: Thumb-1 expectations
Typically we would expect:
  Thumb-1 code to be smaller (use less memory for code) than ARM code with the same functionality
  Thumb-1 code to be slower than comparable ARM code
  Again, this depends on the configuration of the hardware and vagaries of the particular compiler being used.
A 2002 paper by Krishnaswamy and Gupta found Thumb-1 code to be roughly 70% the size of ARM code on average and up to 30% slower. (citation)

## Slide 7: Thumb-2 basics
Thumb-2 essentially adds some 32-bit instructions (called extensions) to the Thumb-1 instruction set.
Different ARM architectures have differing extensions.
The assembler select a proper encoding based on the input instruction and particular hardware being targeted.
https://static.docs.arm.com/ddi0419/d/DDI0419D_armv6m_arm.pdf
http://single-boards.com/armv6-vs-armv7/

## Slide 8: Questions
What sorts of situations might be more sensitive to code size?
  Any code burned into a ROM
  Systems pushing the limit of physical memory
Why might Thumb-1 code actually run faster than ARM code
  Memory system optimized for 16 bit access
  Better i-cache performance

## Slide 9: Lab
In this lab you are given some C code and will build it for ARM, Thumb-1, and Thumb-2.
A makefile is provided for you.
You will:
  Measure the size of the relevant function for the three different ISA’s
  Measure the performance of the code as compiled for the three different ISA’s
  See the 32-bit, 16-bit, and mixed-bit instructions by disassembling the code.
  Summarize your results and answer some questions.